## Slide 1: OSI (Open Systems interconnection) Model

## Slide 2
This are the layers of OSI Model
  Send sends data in “top-down ” approach
  Receiver receives data in “bottom-up approach”
  1st four layers are known as software layer or upper layer where last three layers are known as hardware layer or lower layer
  Transport layer is also known as heart of OSI Model

## Slide 3
This image shows 1st three layer working on Data
4th layer working on Segments
5th layer working on Packets
6th layer working on Frames and at the end 7th layer working on Bits
Data = Packet = segments = frames only name differs according to layers

## Slide 4: Layers With its functions
Application Layer:
  Which is known as Host Layer also and it is used Data as a Protocol Data Unit (PDU).
  Main Tasks:
    High level APIs
    Remote file access
    Internet usage
    Resource sharing
  Protocols:
    HTTP, FTP, HTTPS, SMTP, SSH, Telnet (same as in Presentation Layer and Session Layer)

## Slide 5
Presentation Layer:
  Which is known as Host Layer also and it is used Data as PDU.
  Translation of data between a networking service and an application.
  Main Tasks:
    Translation
    Character encoding
    Data Compression (5 MB file to 2 MB file)
    Conversion (JPEG to PNG, Word to PDF)
    Encryption / Decryption

## Slide 6
Session Layer:
  Which is known as Host Layer also and it is used Data as PDU.
  Managing Communication sessions, i.e. continuous exchange of information in the form of multiple back-and-forth transmission between nodes.
  Ex. Online Transaction Websites
  Main Tasks:
    Managing
    Authentication (Enter login ID and Password)
    Authorization (Successfully login to the account)

## Slide 7
Transport Layer:
  Which is known as Host Layer also and it is used Segment or Datagram as PDU
  Reliable data transmission of data segments between points on a network.
  Protocols:
    TCP(Transmission Control Protocol),
    UDP (User Datagram Protocol)
  Main Tasks:
    Segmentation
    Acknowledgement
    Multiplexing
    End to end Delivery

## Slide 8
Network Layer:
  Which is known as Media Layer also and it is used Packet as PDU.
  Structuring and managing a multi-node network.
  Protocols:
    BGP
    IP
    RIP
    OSPF
    EIGRP
    DHCP
    ICMP
  Main Tasks:
    Addressing
    Routing
    Traffic (Congestion Control)
    Logical Addressing

## Slide 9
Data Link Layer:
  Which is known as Media Layer also and It is used Frames as PDU.
  Reliable transmission of data frames between two nodes connected by a physical layer
  Protocols:
    Ethernet
    FR (Frame Relay)
    MAC
  Main Tasks:
    Physical Addressing

## Slide 10
Physical Layer:
  Which is known as Media Layer also and It is used Bits as a PDU.
  Transmission and reception of raw bit streams over a physical medium.
  It uses Co-axial cable, Fiber cable, RJ-45 etc.
  Main Tasks:
    Media
    Signal
    Binary Transmission